## Slide 1: CanSecWest
Vancouver | 15 March 2017

## Slide 2: Harnessing Intel Processor Trace on Windows for Vulnerability Discovery
Andrea Allievi – Microsoft Ltd
Richard Johnson – Cisco Systems Inc

## Slide 3: Who we are - Richard Johnson
Talos Vulndev
  Third party vulnerability research
    170 bug finds in last 12 months
      Microsoft
      Apple
      Oracle
      Adobe
      Google
      IBM, HP, Intel
      7zip, libarchive, NTP
  Security tool development
    Fuzzers, Crash Triage
  Mitigation development
    FreeSentry
  Research Lead
  Cisco Talos VulnDev

## Slide 4: Who we are - Andrea Allievi
  Italian Security research Engineer, mainly focused on OS Security, Kernel Analysis and Malware Research
  Microsoft OSs Internals enthusiast / Kernel system level developer
  Work for the Threat Intelligence Center of Microsoft Ltd (MSTIC)
  Previously worked for Cisco Systems in the TALOS Security Research and Intelligence Group
  Previously worked for PrevX, Webroot and Saferbytes
  Original designer of the first UEFI Bootkit in 2012, Patchguard 8.1 bypass in 2014, and other research projects/analysis
  Windows Intel Pt Driver designer and developer

## Slide 5: Introduction
  In 2014 - 2016 I have been researching high performance tracing and fuzzing
    2014/2015 - High Performance Fuzzing
    2015/2016 - Go Speed Tracer
  Ruxcon 2015 I demoed a working prototype of Intel PT for coverage fuzzing
  June 2016 we developed a prototype Intel Processor Trace driver for Windows
    The driver has been released open-source:
      https://github.com/intelpt
  This talk picks up where the last one left off…
    See http://moflow.org for previous slides and talk videos
Notes: Interested in DBI (Pin, Dynamorio, Dyninst) or other hardware tracing, see Go Speed Tracer
High Performance Fuzzing: Targeting & Input Selection →Engine Design →Host Configuration
Agenda – Overview of IntelPT, Windows driver implementation details, demos, guided fuzzing, more demos!

## Slide 6: Intel Processor Trace

## Slide 7: Intel Processor Trace
  Intel Processor Trace is a low-overhead hardware execution tracing feature
  It works by capturing information about software execution on each hardware thread using dedicated hardware in the CPU’s Performance Monitoring Unit (PMU)
  After the execution completes software can process the captured trace data and reconstruct the exact program flow
  The trace format is highly compressed for efficient logging and requires some effort to decode
Why is this useful?
  Diagnostic code coverage
  Coverage driven fuzzing – automatically find software vulnerabilities
  Malware analysis – sandboxes can trace malware and feed it to the detection filtering platform
    Current malware does not attempt to discover intelpt tracing*
Notes: Possible timing attacks

## Slide 8: Detecting Intel PT
CPUID with leaf 0x7 can detect the support for Intel PT
If supported, CPUID with leaf 0x14 can return the supported PT features
Different CPUs implement different capabilities
The architecture defines different MSRs to control each tracing operation
Intel initially released Intel PT as part of Broadwell architecture
    Limited tracing and logging modes
Intel expanded on the functionality in Skylake
    Multiple log buffer management modes
Skylake architecture to be available on Xeon CPUs in 2017

## Slide 9: Detecting Intel PT
INTEL_PT_CAPABILITIES ptCap = { 0 };
int cpuid_ctx[4] = { 0 };// EAX, EBX, ECX, EDX
// Processor support for Intel Processor Trace is indicated by
// CPUID.(EAX=07H,ECX=0H):EBX[bit 25] = 1.
__cpuidex(cpuid_ctx, 0x07, 0);
if (!(cpuid_ctx[1] & (1 << 25))) return FALSE;
// Now enumerate the Intel Processor Trace capabilities
RtlZeroMemory(cpuid_ctx, sizeof(cpuid_ctx));
__cpuidex(cpuid_ctx, 0x14, 0);
// If the maximum valid sub-leaf index is 0 exit immediately
if (cpuid_ctx[0] == 0) return FALSE;

## Slide 10: Detecting Intel PT
EAX = 0x14 - Intel Processor Trace
EBX
Bit 00: IA32_RTIT_CTL.CR3Filter can be set to 1
    IA32_RTIT_CR3_MATCH MSR can be accessed.
Bit 01: Configurable PSB and Cycle-Accurate Mode.
Bit 02: IP Filtering, TraceStop filtering, and preservation of Intel PT MSRs across warm reset.
Bit 03: MTC timing packet and suppression of COFI-based packets.
ECX
Bit 00: Tracing can be enabled with IA32_RTIT_CTL.ToPA = 1 utilizing the ToPA output scheme
    IA32_RTIT_OUTPUT_BASE and IA32_RTIT_OUTPUT_MASK_PTRS MSRs can be accessed.
Bit 01: ToPA tables can hold any number of output entries
    Maximum specified by the MaskOrTableOffset field of IA32_RTIT_OUTPUT_MASK_PTRS.
Bit 02: Single-Range Output scheme.
Bit 03: Output to Trace Transport subsystem.
Bit 31: Generated packets which contain IP payloads have LIP values
    Includes the CS base component
Notes: SKIP

## Slide 11: Detecting Intel PT
EAX = 0x14 - Intel Processor Trace
Packet Generation (ECX = 1)
EAX
Bits 2:0: Number of configurable Address Ranges for filtering.
Bit 31:16: Bitmap of supported MTC period encodings
EBX
Bits 15-0: Bitmap of supported Cycle Threshold value encodings
Bit 31:16: Bitmap of supported Configurable PSB frequency encodings
Notes: SKIP

## Slide 12: Why is Intel PT so interesting?
Implemented entirely in hardware
You can trace all software that the CPU runs (except for SGX secure containers)
Suppose you have to analyze an hypervisor or an evil SVM handler
    With Intel PT you can do that!
  Performance
    Low over-head (15% CPU perf hit for recording)
    Logs directly to physical memory, bypassing TLB and eliminating cache pollution
    Minimal log format takes little time to record
      One bit per conditional branch
      Only indirect branches log dest address

## Slide 13: How it works - Summary
Different kinds of trace filtering:
    Current Privilege Level (CPL) – used to trace all of user or kernel
    PML4 Page Table – used to trace a single process
    Instruction Pointer – used to trace a particular slice of code (or module)
Two types of output logging:
    Single Range
    Table of Physical Addresses
Notes: PML4 = Page Map Level 4 points to page directory

## Slide 14: Single Range
OS should allocate a contiguous physical memory buffer (MmAllocateContiguousMemory is a good fit)
This mode is best suited for
    Tracing of single application with sufficient size of buffer
    Redirect the output to a MMIO port or some JTAG controllers
    Always-On tracing for post-mortem or forensic analysis
  To enable:
    Set the proper MSRs
      MSR_IA32_RTIT_OUTPUT_BASE and MSR_IA32_RTIT_OUTPUT_MASK_PTRS
  Start the Tracing by setting the “TraceEn” flag in the control register
  The buffer will be filled by the processor in a circular-manner
Notes: Linux kernel perf supports a circular buffer which can be loaded into GDB

## Slide 15: Table of Physical Addresses
Table of Physical Addresses (aka ToPA) is a list of tables that describes each physical address used for storing the trace
A well-known data-structure definition PML4 (see the Intel Manual)
This allows the processor to write data to non-contiguous memory regions
Binary compatibility with the “MDL” data structure of Windows kernel
Modality best suited for:
    Tracing big code areas and/or dump the results in a user-mode file
    Supporting pause/resume of a application and on-the-fly analysis of the dump
  Very powerful – an Interrupt could be generated by the processor at a certain point if the buffer is going to be full, or STOP signal

## Slide 16: Different type of Trace Packets
  Packet Stream Boundary (PSB) packets - ‘heartbeats’ that are generated at regular intervals (configurable), synchronization points for the decoder
  Paging Information Packets (PIP) - record modifications made to the CR3 register
  Timing packets (TSC, MTC & CYC) packets - helps in tracking wall-clock time (related to events or not)
  Control flow packets: taken-not-taken (TNT), target IP (TIP), Flow update (FUP), MODE packets
  Core bus ratio packets: highlights modifications in the CPU clock
  Overflow packets: sent when the processor encounters an internal buffer overflow
  In our driver the user can decide if enable or not the generation of some kind of packets (control flow – TSC/MTC/CYC)
  * Refer to the Intel’s manual for the details
Notes: COFI = Change of Flow instruction
Paging Information Packet (PIP) - PIPs record modifications made to the CR3 register. This information, along with info from the OS on the CR3 value of each process, allows the debugger to attribute linear addresses to their correct application source.
Explain the difference between TSC (bound an event to a time) and MTC (mini time counter - a periodic indication of wall-clock time)
Explain the difference between TIP and FUP packets (TIP – Indirect Transfer COFI; FUP – Async Events)

## Slide 17: Different type of Trace Packets
Notes: Paging Information Packet (PIP) - PIPs record modifications made to the CR3 register. This information, along with info from the OS on the CR3 value of each process, allows the debugger to attribute linear addresses to their correct application source.
Explain the difference between TSC and MTC (mini time counter)
Explain the difference between TIP and FUP packets (TIP - ; FUP - )

## Slide 18: Windows Intel PT Driver

## Slide 19: The Project
We have decided to write a Windows driver, with the goal of supporting all trace and filtering modes for kernel and userspace
At the time of this writing the driver is in version 0.5
  Supports all the filtering mode combinations and both output modes
  Supports multi-processors
  Supports kernel mode code tracing and kernel mode API
Some issues had been resolved:
  APIC controller programming for the PMI interrupt notification
  User-mode buffer mapping
  Multi processor issues
  How to trace spawned processes

## Slide 20: The PMI Interrupt
The ToPA output scheme supports a mode in which the CPU triggers a PMI (performance monitor interrupt) every time the buffer is full*
We would like to enable and connect to that interrupt
In that way we can process the trace content when buffer is full
To control the traced process, either
  Use a hypervisor -> VMEXIT
  Suspend the target process from kernel, dump the trace data and resume
Another problem here: the IRQL in which the code runs is HIGH_LEVEL
Solved dividing the job in 3 phase: PMI Handler -> DPC -> Work Item
Connecting the ISR and find a way to map the IoApic memory space have been not an easy task
Notes: PMI Handler = checks that the interrupt is the PT one (checking the LVT table), re-masks the interrupt – queue a DPC
DPC Routine – Set the PMI event – queue a Work Item
Work Item – Suspend the User-mode process
Connect the ISR: IoConnectInterrupt requires a physical device object – Solution: use HalSetSystemInformation(HalProfileSourceInterruptHandler, sizeof(PMIHANDLER), …)

## Slide 21: The User mode buffer
Processor Trace works with physical addresses - not Virtual addresses
ToPAs describe a big buffer composed by different smaller physical chunks.
Need a way to create a big virtual buffer composed by each chunk and map this to user-mode in a very secure manner (otherwise the driver will be subject of kernel-exploitation)
Intel is not stupid. The ToPA and the MDL data structures are compatible
Solution:
  allocate physical memory using the OS facilities*
  Convert the MDL descriptor into ToPA entries
  Securely map the final virtual buffer using the OS
Notes: Alloc physical pages: MmAllocatePagesForMdlEx and MmGetMdlPfnArray
Map the physical MDL to User mode: MmMapLockedPagesSpecifyCache

## Slide 22: Multi-Processor and Multi Thread support
New feature in version 0.5
Each processor has an associated PT Buffer mapped in the target user-mode process (but not in kernel-mode)
Only an event signaled when the PMI Interrupt fires was not enough
  Introduced the User-mode callbacks – a smart method to manage the PT log directly from User-mode
Still some problems in managing multi-threaded and multi process application

## Slide 23: Kernel mode Tracing
New feature in version 0.5
The Driver is able to perform the tracing of Kernel mode code in 2 ways
  From the user-mode application (executed with Admin privileges) -> Uses IP filtering mode
  From another kernel-mode driver -> the driver must use the exported APIs and manage the PT buffer(s), and multi-processor stuff on its own
In this way we have been able to perform the trace of:
  The loading / unloading of a new Kernel module
  Some IOCTL called by a test user application

## Slide 24: The client code
Quite a simple setup:
Get an handle to the PT Device
hPtDev = CreateFile(L"\\\\.\\WindowsIntelPtDev", FILE_ALL_ACCESS, 0, NULL,
OPEN_EXISTING, 0, NULL);
Spawn the process / decide what to trace and set the options in the PT_USER_REQ data structure (process ID, CPU Affinity mask, buffer size, …)
Start the tracing
    DeviceIoControl(hPtDev, IOCTL_PTDRV_START_TRACE, (LPVOID)&ptStartStruct,
    sizeof(PT_USER_REQ), lpPtBuffArray, sizeof(LPVOID) * dwNumOfCpus,
    &dwBytesIo, NULL);
Stop the trace and clear the resources (important)
bRetVal = DeviceIoControl(hPtDev, IOCTL_PTDRV_CLEAR_TRACE,
(LPVOID)&dwTargetCpu, sizeof(DWORD), NULL, 0, &dwBytesIo, NULL);

## Slide 25: The Multiprocessor client code
Spawn a new thread for each CPU
To register the user-mode callback use the new PTDRV_REGISTER_PMI_ROUTINE IOCTL code (one call for each thread)
Specify an affinity mask composed by only the executing processor ID
Perform a wait in an alertable state
That’s all!
Your User-mode callback will be called each time the CPU trace buffer will become full

## Slide 26: Some other challenges
CR3 physical page swappable?
  Quick analysis shows that in Windows 10586
    Only the main PML4 table page is always in memory
Otherwise make use of the PIP packets
The problem of the spawned processes has been resolved using the trace by IP – detect when a new process is spawned and add the new range
OR
Use the tracing by CPL and parse the PIP packets
Notes: * Explain this

## Slide 27: Demo

## Slide 28
Vulnerability Discovery
Now we have a fast tracing engine
How will we utilize it for vulnerability discovery?

## Slide 29
Evolutionary Fuzzing
Incrementally better mutational dumb fuzzing
Trace while fuzzing and provide feedback signal
Evolutionary algorithms
  Assess fitness of current input
  Manage a pool of possible inputs
Focused on security bugs

## Slide 30
Evolutionary Fuzzing
From previous research, these are the required components
  Fast tracing engine
    Block based granularity
  Fast logging
    Memory resident coverage map
  Fast evolutionary algorithm
    Minimum of global population map, pool diversity

## Slide 31
Amercian Fuzzy Lop
Michal Zalewski 2013
  Delivered the first performant opensource evolutionary fuzzer
Features
  Uses variety of traditional mutation fuzzing strategies
  Block coverage via compile time instrumentation
  Simplified approach to genetic algorithm
    Edge transitions are encoded as tuple and tracked in a bloom filter
    Includes coverage and frequency
  Uses portable* Posix API for shared memory, process creation

## Slide 32
Amercian Fuzzy Lop
Contributions
  Tracks edge transitions
    Not just block entry
  Global coverage map
    Generation tracking
  Fork server
    Reduce fuzz target initialization
  Persistent mode fuzzing
  Builds corpus of unique inputs reusable in other workflows

## Slide 33
Amercian Fuzzy Lop
Trace Logging
  Each block gets a unique ID
  Traversed edges are indexed into a bloom filter map
  Create a hash from the src and dst block IDs
  Increment map for each time an edge is traversed
  Each trace is easily comparable to the entire session history

## Slide 34
Windows Evolutionary Fuzzing
Started research into this area in 2015
  High Performance Fuzzing
  Go Speed Tracer
Windows Software primarily distributed as binaries
  High speed binary code coverage required
Seemed like a good opportunity to use Intel Processor Trace
  First prototyped on Linux using simple-pt
  Demoed Linux afl-intelpt at Ruxcon 2015
Lack of a usable driver for Windows lead to partnership with Andrea

## Slide 35
WinAFL
Ivan Fratric July 2016
  First performant windows evolutionary fuzzer
Features
  Its American Fuzzy Lop! For Windows!
  Windows API port for memory and process creation
  DynamoRIO based code coverage
  Filter based on module
  Block and Edge tracing modes
    Block tracing by default due to issues with multi-threading
  Persistent execution mode

## Slide 36
WinAFL
Ivan Fratric July 2016
  First performant windows evolutionary fuzzer
Persistence
  Multiple inputs can be parsed without exiting the process
  DynamoRIO allows hooking of target function
    User specifies address and number of arguments
    On function exit, WinAFL repopulates args and loops function
    User specifies number of loops before process restart

## Slide 37
WinAFL
Ivan Fratric July 2016
  First performant windows evolutionary fuzzer
Persistence is key
    Restart process each time (disable persistence) ~2.3 exec/s
    Persist 100 iterations before restart ~72 exec/s
    Persist 1000 iterations ~123 exec/s
    Persist 10000 iterations ~133 exec/s

## Slide 38
WinAFL IntelPT
Richard Johnson 2016
  Windows hardware driven evolutionary fuzzer
Key problems to solve
  The IntelPT log does not contain Block IDs or all branch targets
  Parsing large compressed logs is time consuming
  Native persistence mode is not yet implemented
    *Work in progress using Avrf as hooking engine
  We can filter up to 4 address ranges or whole process

## Slide 39
WinAFL IntelPT
Richard Johnson 2016
  Windows hardware driven evolutionary fuzzer
Current status
  WinAFL IntelPT now accurately decodes full trace
  The TIP packet of IntelPT holds target addresses
    Generated for indirect branches and return
  The TNT packets are conditional branch states
    We must disassemble from last known IP to recover conditional branch target
    We use a discovered branch cache to reduce disassembly time (needs persist to disk*)
  Edge src/dst encoded into AFL bloom filter
  We currently use CreateProcess and WaitForSingleObject
    See Go Speed Tracer for experiments in Windows fork()

## Slide 40
WinAFL IntelPT
Performance
  Dummy loop benchmark
  CreateProcess / Wait
  85 exec/sec
american fuzzy lop 1.96b (test_gdiplus.exe)
+- process timing -------------------------------------+- overall results ----+
| run time : 0 days, 0 hrs, 1 min, 0 sec | cycles done : 0 |
| last new path : none seen yet | total paths : 10 |
| last uniq crash : none seen yet | uniq crashes : 0 |
| last uniq hang : none seen yet | uniq hangs : 0 |
+- cycle progress --------------------+- map coverage -+----------------------+
| now processing : 7* (70.00%) | map density : 1 (0.00%) |
| paths timed out : 0 (0.00%) | count coverage : 1.00 bits/tuple |
+- stage progress --------------------+ findings in depth --------------------+
| now trying : havoc | favored paths : 1 (10.00%) |
| stage execs : 1272/2500 (50.88%) | new edges on : 1 (10.00%) |
| total execs : 4945 | total crashes : 0 (0 unique) |
| exec speed : 85.16/sec (slow!) | total hangs : 0 (0 unique) |
+- fuzzing strategy yields -----------+---------------+- path geometry -------+
| bit flips : 0/64, 0/62, 0/58 | levels : 1 |
| byte flips : 0/8, 0/6, 0/2 | pending : 9 |
| arithmetics : 0/446, 0/74, 0/5 | pend fav : 0 |
| known ints : 0/45, 0/187, 0/79 | own finds : 0 |
| dictionary : 0/0, 0/0, 0/0 | imported : n/a |
| havoc : 0/2500, 0/0 | variable : 0 |
| trim : 99.93%/36, 0.00% +-----------------------+
+-----------------------------------------------------+

## Slide 41
WinAFL IntelPT
Performance
  Trace enabled
  No log parsing
  72 exec/sec
  15% tracing overhead
american fuzzy lop 1.96b (test_gdiplus.exe)
+- process timing -------------------------------------+- overall results ----+
| run time : 0 days, 0 hrs, 1 min, 0 sec | cycles done : 0 |
| last new path : none seen yet | total paths : 10 |
| last uniq crash : none seen yet | uniq crashes : 0 |
| last uniq hang : none seen yet | uniq hangs : 0 |
+- cycle progress --------------------+- map coverage -+----------------------+
| now processing : 7* (70.00%) | map density : 1 (0.00%) |
| paths timed out : 0 (0.00%) | count coverage : 1.00 bits/tuple |
+- stage progress --------------------+ findings in depth --------------------+
| now trying : havoc | favored paths : 1 (10.00%) |
| stage execs : 763/2500 (30.52%) | new edges on : 1 (10.00%) |
| total execs : 4436 | total crashes : 0 (0 unique) |
| exec speed : 72.19/sec (slow!) | total hangs : 0 (0 unique) |
+- fuzzing strategy yields -----------+---------------+- path geometry -------+
| bit flips : 0/64, 0/62, 0/58 | levels : 1 |
| byte flips : 0/8, 0/6, 0/2 | pending : 9 |
| arithmetics : 0/446, 0/74, 0/5 | pend fav : 0 |
| known ints : 0/45, 0/187, 0/79 | own finds : 0 |
| dictionary : 0/0, 0/0, 0/0 | imported : n/a |
| havoc : 0/2500, 0/0 | variable : 0 |
| trim : 99.93%/36, 0.00% +-----------------------+
+-----------------------------------------------------+

## Slide 42
WinAFL IntelPT
Performance
  Full tracing and parsing
  55 exec/sec
  22% parsing overhead
  Total of ~35% overhead
american fuzzy lop 1.96b (test_gdiplus.exe)
+- process timing -------------------------------------+- overall results ----+
| run time : 0 days, 0 hrs, 1 min, 0 sec | cycles done : 0 |
| last new path : 0 days, 0 hrs, 0 min, 0 sec | total paths : 48 |
| last uniq crash : none seen yet | uniq crashes : 0 |
| last uniq hang : none seen yet | uniq hangs : 0 |
+- cycle progress --------------------+- map coverage -+----------------------+
| now processing : 0 (0.00%) | map density : 2594 (3.96%) |
| paths timed out : 0 (0.00%) | count coverage : 1.49 bits/tuple |
+- stage progress --------------------+ findings in depth --------------------+
| now trying : calibration | favored paths : 9 (18.75%) |
| stage execs : 20/40 (50.00%) | new edges on : 47 (97.92%) |
| total execs : 3359 | total crashes : 0 (0 unique) |
| exec speed : 55.81/sec (slow!) | total hangs : 0 (0 unique) |
+- fuzzing strategy yields -----------+---------------+- path geometry -------+
| bit flips : 0/0, 0/0, 0/0 | levels : 2 |
| byte flips : 0/0, 0/0, 0/0 | pending : 48 |
| arithmetics : 0/0, 0/0, 0/0 | pend fav : 9 |
| known ints : 0/0, 0/0, 0/0 | own finds : 37 |
| dictionary : 0/0, 0/0, 0/0 | imported : n/a |
| havoc : 0/0, 0/0 | variable : 47 |
| trim : 0.00%/1341, n/a +-----------------------+
+-----------------------------------------------------+

## Slide 43: Demo
WinAFL + IntelPT

## Slide 44: Conclusions
Tracing is used very often in fuzzing and dynamic analysis
Intel Processor Trace is a promising mechanism for hardware tracing
Intel is dedicated to producing high performance trace features
TODO List:
  Implement thread context switch tracing in a reliable way (ETW)
  Modify a Hypervisor to be able to use Intel PT inside a Guest VM
  Understand how to trace VMM, SMM code and test with SGX software
  Enable persistent mode in native apps with Intel PT

## Slide 45
Thank you!
https://github.com/intelpt
@richinseattle / rjohnson@moflow.org
@aall86
Questions?

## Slide 46: Multi-Threaded and Multi-Process applications
Always increasing in their number (think about AppContainer or Browsers for example)
A simple solution resides in the log parser:
  Make use of the PIP (Page information packets) to identify each process
Big drawbacks: the size of the log is HUGE – the time needed to parse it is even MORE
Register a Process / Thread Creation callback in Kernel mode and trace one process per time
  Simple solution, log size still acceptable
  Some malware or complex applications requires process interactions
BUT …

## Slide 47: In the beginning was a PUSHAD …
Do you remember the old glorious PUSAHD instructions?
From the Intel manuals: “Pushes the contents of the general-purpose registers onto the stack.”
No equivalence for X64 registers or Kernel MSR
I was studying how to trace only a single thread, intercepting the Windows Thread Context Switcher
Someone has pinpoint to me the existence of another very-cool instruction in the AMD64 architecture, but no so known by the research community
Special thanks to Xinyang Ge of Microsoft Research for signaling this

## Slide 48: … and now it is XSAVE
Saves some processor state components to the XSAVE area
MMX, SSE, AVX, AVX-512 user mode registers (What a heck is AVX-512?)
… and even the new CPU registers that belongs to Intel PT and Intel MPX
New CPUID leaf functions for compatibility verification, new CPUs opcodes
Basically is a very fast way to save even X64 Kernel-accessible Register in a particular memory buffer
To use this feature in user-mode you have to fill the XCR0 register with XSETBV instruction
Instead for kernel mode staff, you have to fill a special MSR register: IA32_XSS (number 0x0DA0)
Finally a call to the XSAVE (or XSAVES if in Kernel mode) fills the buffer with the needed information *
Notes: * Refer to the Intel Manual for the implementation details

## Slide 49: Thread tracing
Originally I planned to manual save each Intel PT MSRs after intercepting the thread context switcher
While analyzing the Windows 10 Context Switcher, I realized that it already supports the XSAVE feature
2 solutions -> We conclude that it was not feasible in a very stable manner:
  Find a way to hook or divert the KeSwapContext routine -> No public-available method -> Patchguard become angry
  Use ETW
Research still in progress!